## Slide 1: EERF 6395: RF and Microwave Systems Engineering Final Project
GROUP 2
Nadiah Sarfraz (5G TX) Niyati Sanandiya (Radar RX ) Nirjari Shukla (5G RX) Varsha Paul (Radar TX)
INTELLIGENT HAILSTORM DETECTION AND WARNING SYSTEM

## Slide 2: Table of Contents
Problem Statement & Solution
System Architecture
Radar Block Diagram
Communication Link Block Diagram
Radar TX Channel
5G Communication RX Channel
Drone Specifications
System Issues
Project Implementation Plan

## Slide 3: Problem Statement
In 2017, National Oceanic and Atmospheric Administration, NOAA’s National Weather Service estimated about 6045 hailstorms.
In 2016, Hailstorms caused about 21 injuries , around $3.51 billion property damage, 23.73 million crop damage, which gives total of $3.53 billion damage.
Texas suffered from Hail damage cost of approximately $138,539 in 2015.

## Slide 4: Solution
Our system aims at reducing these damages as much as possible by proactively detecting hail and sending alert messages to people.
Drone detects weather condition by an inbuilt radar system and triggers the communication link.
Weather monitoring station sends alert messages to people using 5G communication link.
Weather warnings can help people protect themselves and their property from adverse weather conditions.

## Slide 5: System Architecture
Weather condition
Drone triggers communication link
Base station
5G communication link
RADAR

## Slide 6: Top-level Radar Specs
Parameter | Top-level Spec | Min/ Max
Frequency Band (GHz) | 14.5-15.5 | Min
Transmit Output Power (dBm) | 25 | Min
Transmit Channel Gain (dB) | 35 | Min
Transmit Channel PAE (%) | 35 | Min
Receive Noise Figure (dB) | 4.5 | Max
Receive Channel Gain (dB) | 35 | Min
Receive Channel OIP3 (dBm) | 25 | Min
Antenna Beamwidth (degrees) | +/-20 | Max
Range (m) with Target RCS=1.0m | 250 | Min
Total DC Power Consumption (W) | 10 | Max

## Slide 7
Top-level Communication link Specifications
Parameter | Top-level Spec | Min/ Max
Frequency Band (GHz) | 23-25 | Min
Transmit Output Power (dBm) | 25 | Min
Transmit Channel Gain (dB) | 15 | Min
Transmit Channel PAE (%) | 25 | Min
Receive Noise Figure (dB) | 5 | Max
Receive Channel Gain (dB) | 15 | Min
Receive Channel OIP3 (dBm) | 20 | Min
TX Antenna Az Beamwidth (degrees) | +/-5 | Max
RX Antenna Az Beamwidth (degrees) | +/-5 | Max
Range (m) | 5000 | Min
Total DC Power Consumption (W) | 10 | Max

## Slide 8: RADAR TRANSMITTER
SIGNAL
SOURCE
LPF
BPF
PA
MIXER
ANTENNA
LOCAL OSCILLATOR
IF
PA
DA

## Slide 9: RADAR RECEIVER
IF BPF
Received Signal
IF
Image Reject Filter
LNA
ANTENNA
MIXER
LOCAL OSCILLATOR
BPF

## Slide 10: RADAR TRANSCEIVER
CIRCULATOR
LOCAL OSCILLATOR
LNA
Image Reject
Filter
IF BPF
IF
Received Signal
BPF
SIGNAL
SOURCE
LPF
BPF
MIXER
IF
PA
DA

## Slide 11: COMMUNICATION LINK TRANSMITTER
SIGNAL
INPUT
MODULATOR
BPF
MIXER
ANTENNA
PA
LPF
LOCAL OSCILLATOR
DA
IF

## Slide 12: COMMUNICATION LINK RECEIVER
LPF
IF
DEMODULATOR
PROCESSING UNIT
Image Reject Filter
LNA
ANTENNA
MIXER
LOCAL OSCILLATOR
BPF

## Slide 13
RADAR LINK

## Slide 14: RADAR TRANSMITTER SCHEMATIC

## Slide 15: Cascaded Gain (C_GP) (dB)

## Slide 16: Yield Analysis Cascaded Gain (C_GP) (dB)

## Slide 17: Cascaded Node Power (P_node) (dBm)

## Slide 18: Yield Analysis Cascaded Node Power (P_node) (dBm)

## Slide 19
Components used in
Radar Transmitter

## Slide 20: .
OPERATING FREQUENCY RANGE | 0-20 Ghz
GAIN(dB) | 19.5
NOISE FIGURE(dB) | 1.9
P1 dB(dB) | 25
DRIVER AMPLIFIER

## Slide 21: .
OPERATING FREQUENCY RANGE | 0.4-1.4 Ghz
INSERTION LOSS(dB) | 1.43

## Slide 22: .
OPERATING FREQUENCY RANGE | 3-20 Ghz
CONVERSION LOSS | 9 dB
LTC 5553
MIXER

## Slide 23: .
OPERATING FREQUENCY RANGE | 14.5-15.5 Ghz
LOSS | 3 dB
BANDPASS FILTER

## Slide 24: .
OPERATING FREQUENCY RANGE | 11-17 Ghz
GAIN | 27 dB
P1dB | 27 dB
NOISE FIGURE | 3
TGA 2565-SM
POWER AMPLIFIER

## Slide 25: .
OPERATING FREQUENCY RANGE | 14.4-15.4 Ghz
GAIN | 24 dB
P1dB | 34.5 dB
NOISE FIGURE | 7 dB
MAAP-010517

## Slide 26: Power Added Efficiency Calculation
Pin=1.258 mW
Pout=4822.16 mW
Pdc=1W+1.6W+0.436W+6W+1.260W+1W
=11.296W
PAE=(Pout-Pin)/Pdc*100 %
=(4822.16-1.258)/11.296 * 100 %
PAE =42.67%

## Slide 27: EIRP(Effective Isotropic Radiated Power)
Pt= 36.83 dB => 4822.16 mW
Gt=20 dB =>100(in Linear)
EIRP= Pt+ Gt
=36.83+20 dBm
=56.83 dBm
EIRP(in W)=481.94 W
EIRP(in dBW)=26.83 dBW

## Slide 28: RADAR RECEIVER SCHEMATIC

## Slide 29: Cascaded Gain (C_GP) (dB)

## Slide 30: Yield Analysis Cascaded Gain (C_GP) (dB)

## Slide 31: Cascaded Noise Figure (C_NF) (dB)

## Slide 32: Yield Analysis Cascaded Noise Figure (C_NF) (dB)

## Slide 33: Cascaded IP3 (C_IP3) (dBm)

## Slide 34: Yield Analysis Cascaded IP3 (C_IP3) (dBm)

## Slide 35
Components used in
Radar Receiver

## Slide 36: LOW PASS FILTER
OPERATING FREQUENCY RANGE | 0-1.2 Ghz
INSERTION LOSS | 0.7 dB
SKU-0711-025

## Slide 37: LOW NOISE AMPLIFIER
OPERATING FREQUENCY RANGE | 2-22 Ghz
GAIN | 15 dB
P1dB | 22 dB
NOISE FIGURE | 2 dB
TGA-2227-5M

## Slide 38: LOW NOISE AMPLIFIER
OPERATING FREQUENCY RANGE | 7-16 Ghz
P1dB | 18 dBm
GAIN | 27 dB
NOISE FIGURE | 1.1 dBm
QPA-2609D

## Slide 39: Bandpass filter
OPERATING FREQUENCY RANGE | 12-18 Ghz
CONVERSION LOSS | 3 dB

## Slide 40: MIXER
LTC 5553
OPERATING FREQUENCY RANGE | 3-20 Ghz
CONVERSION LOSS | 9 dB

## Slide 41: POWER AMPLIFIER
OPERATING FREQUENCY RANGE | 1-18 Ghz
GAIN | 30 dB
P1dB | 19 dB
NOISE FIGURE | 3.2 dB
PE 15A3262

## Slide 42: POWER AMPLIFIER
OPERATING FREQUENCY RANGE | 12-18Ghz
GAIN | 20 dB
P1dB | 37 dBm
NOISE FIGURE | 1.5 dB

## Slide 43: CIRCULATOR
OPERATING FREQUENCY RANGE | 14-18Ghz
GAIN | -0.6 dB
P1 Db | 20 dB
NOISE FIGURE | 3 dB
KTMC-1502A2

## Slide 44: HAND CALCULATIONS
Pt= 36.83 dB => 4822.16 mW
Gt=Gr=20 dB =>100(in Linear)
F=15 Ghz, λ=0.02
σ =1
R=100 m
=/ *
= (4822.16** *1)/ *
=-70.12 dBm
MDS(No) or = kToB =1.38* *310*
= 4.278* =>-83.69 dBm
Rmax = / *
= ((4822.16** *1)/ *
Rmax =218.41 m

## Slide 45: Free space path loss Calculation
R=100 m, =c/f,
=(3* )/(15* )=0.02 m
=
=
= 95.959 dBm
95.959 dBm

## Slide 46: RADAR TRANSCEIVER SCHEMATIC

## Slide 47: FSPL
MDS=-83.69dBm
FSPL

## Slide 48
5G COMMUNICATION LINK

## Slide 49: 5G COMMUNICATION LINK TRANSMITTER SCHEMATIC

## Slide 50: Cascaded Gain (C_GP) (dB)

## Slide 51: Yield Analysis Cascaded Gain (C_GP) (dB)

## Slide 52: Cascaded Node Power (P_node) (dBm)

## Slide 53: Yield Analysis Cascaded Node Power (P_node) (dBm)

## Slide 54: Pdc = (5V*240mA) + (5V*650mA) + (4.5V * 50mA) = 4675mW Pout = 31.53dBm =1422.32 mW Pin = Pout – Gain = (31.53dBm – 30.53 dB) = 1 dBm = 1.25 mW PAE = ((Pout – Pin) / Pdc)*100 = 30.39% EIRP = Pt (dBm) + Gt (dB) = 31.53+ 24.7 dB = 56.23 dBm = 26.23 dBW (419.75 W)
5G Tx Channel Calculations

## Slide 55: Components Used in 5G Transmitter

## Slide 56
Frequency | 1 GHz – 2 GHz
Gain | 16.5
Noise Figure | 0.23
CGY2151HV_C1

## Slide 57: Band Pass Filter
Frequency | 1.71 Ghz to 1.88 Ghz
Insertion Loss | 2 dB

## Slide 58: Mixer
RF frequency | 2 GHz -26 GHz
IF frequency | 1-15 Ghz
LO frequency | 2-26 Ghz
Conversion Loss | 12 dB
P1dB | 10 dBm

## Slide 59: Band Pass Filter
Frequency | 18 Ghz to 30 Ghz
Insertion Loss | 1.2 dB

## Slide 60: Driver Amplifier
Frequency range | 17 Ghz to 43 Ghz
Gain | 20 dB
P1dB | 19.5 dBm
Noise Figure | 7dB

## Slide 61: Power Amplifier
Frequency | 18 to 26 GHz
Gain | 28.5 dB
IP3 | 37 dBm
P1dB | 28.5 dBm

## Slide 62: 5G COMMUNICATION LINK RECEIVER SCHEMATIC

## Slide 63: Cascaded Gain (C_GP) (dB)

## Slide 64: Yield Analysis Cascaded Gain (C_GP) (dB)

## Slide 65: Cascaded Noise Figure (C_NF) (dB)

## Slide 66: Yield Analysis Cascaded Noise Figure (C_NF) (dB)

## Slide 67: Cascaded IP3 (C_IP3) (dBm)

## Slide 68: Yield Analysis Cascaded IP3 (C_IP3) (dBm)

## Slide 69: Components used in 5G Receiver

## Slide 70: Band Pass Filter
Frequency | 18 Ghz to 30 Ghz
Insertion loss | 1.2 dB

## Slide 71: Low Noise Amplifier
Frequency | 22 Ghz to 32 Ghz
Noise Figure | 1.6 dB
Gain | 23 dB

## Slide 72: Mixer
Rf frequency | 15 GHz -50 GHz
IF frequency | DC-5 Ghz
LO frequency | 15-50 Ghz
Conversion Loss | -10 dB
P1dB | 10 dBm

## Slide 73: Band Pass Filter
Frequency | 18 GHz to 32 GHz
insertion loss | 1.5 dB

## Slide 74: Low Noise Amplifier
Frequency | 15 Mhz to 3 Ghz
Gain | 38 dB
P1dB | 15 dBm

## Slide 75: Band Pass Filter
frequency | 1.7 Ghz to 1.88 Ghz
center frequency | 1.8 GHz
insertion loss | 0.75 dB

## Slide 76: HAND CALCULATIONS
R=5000 m, λ = = = 0.0125 m
FSPL = 20log() = 20log( = 134.02 dB
Pr (dBm) = Pt(dBm)+Gr(dB)+Gt(dB)-FSPL
= 31.53+24.7+20-134.02
Pr (dBm) = -57.79 dBm

## Slide 77: 5G TRANSCEIVER SCHEMATIC

## Slide 78: FSPL
FSPL
MDS=-83.69dBm

## Slide 79: RADAR COMPLIANCE MATRIX
Parameter | Top-level Spec | Modified Spec | Min/ Max | Simulated Performance | Compliant (Y/N)
Frequency Band (GHz) | 14.5-15.5 | 14.5-15.5 | Min | 14.5-15.5 | Y
Transmit Output Power (dBm) | 12 | 25 | Min | 36.83 | Y
Transmit Channel Gain (dB) | 25 | 35 | Min | 36.39 | Y
Transmit Channel PAE (%) | 35 | 35 | Min | 42.67 | Y
Receive Noise Figure (dB) | 4.5 | 4.5 | Max | 1.656 | Y
Receive Channel Gain (dB) | 35 | 35 | Min | 66.7 | Y
Receive Channel OIP3 (dBm) | 20 | 20 | Min | 22.97 | N
Antenna Beamwidth (degrees) | 55 | 20 | Max | 18.9 | Y
Range (m) with Target RCS=1.0m | 250 | 250 | Min | 218.41 | N
Total DC Power Consumption (W) | 10 | 10 | Max | 11.29 | N

## Slide 80: 5G COMMUNICATION LINK COMPLIANCE MATRIX
Parameter | Top-level Spec | Modified Spec | Min/ Max | Simulated Performance | Compliant (Y/N)
Frequency Band (GHz) | 23-25 | 23-25 | Min | 23-25 | Y
Transmit Output Power (dBm) | 25 | 25 | Min | 31.53 | Y
Transmit Channel Gain (dB) | 15 | 15 | Min | 30.53 | Y
Transmit Channel PAE (%) | 25 | 25 | Min | 30.39 | Y
Receive Noise Figure (dB) | 5.0 | 5.0 | Max | 3.017 | Y
Receive Channel Gain (dB) | 15 | 15 | Min | 67.2 | Y
Receive Channel OIP3 (dBm) | 20 | 20 | Min | 24.803 | Y
TX Antenna Az Beamwidth (degrees) | +/-5 | +/-5 | Max | 17.5 | N
RX Antenna Az Beamwidth (degrees) | +/-5 | +/-5 | Max | 17.5 | N
Range (m) | 5000 | 5000 | Min | 5000 | Y
Total DC Power Consumption (W) | 10.0 | 10.0 | Max | 4.675 | Y

## Slide 81
Drone Specifications
Parameter | Top-level Spec
Maximum Range | 7000m
Cost | $31721
Cameras | 2x RED for 3D, Arri Alexa, Alexa M, F55
Payload capacity | 100lb safe (140lb stress)
Auto Return to Home | One-Key Go-Home
Operating Temp | 23 to 140 deg. F
Gear | Intelligent Landing Gear Function
xFold Dragon Drone

## Slide 82: UNIQUE FEATURES
Monitoring is possible due to the GPS feature present in the drone.
The drone has built in sensors and bright LEDs that prompts the status and remaining power of the battery in real time.
Drone continuously calculates its current distance from base station and the amount of power needed to return.
Alarm system is included to scare off the birds.
Our system uses a single drone for a given area. However, it can be expanded to have a network of drones working ‘smartly’ to detect hail.

## Slide 83
Batteries for Drones
Brand | VENOM
Batteries material | Li-Po
Capacity | 22000mAh
Charge Rate | 1C (22 A)
Flight Duration | 60 Minutes
Weight | 2749g
Application | Drone

## Slide 84
Battery Calculations
Total DC power of the RF components in the radar channels= Pdc = 20.98 W
Energy consumed in one flight duration: (Pdc * flight time) = (20.98 W * 60 mins)
= 20.98 Wh = 20980 mWh
Required Battery Capacity = Energy Consumed / Battery Voltage
= 20980 mWh / 22.2 V = 9536.36 mAh
Drone with a battery having capacity of 22000 mAh is used
Required Battery Capacity < Supplied Battery Capacity
The batteries on the drone supply enough power to the RF components

## Slide 85
Bandwidths and Operating frequency chosen comply to the FCC regulations
According to IEEE health standards the power radiated should be less than 10 mW/sq.cm
Power radiated for the radar = 6.13x10-5 mW/sq.cm ( for 250m)
Power radiated for Comm link = 1.31x10-7 mW/sq.cm ( for 5000m)
Power radiated for the radar = 3.83x10-4 mW/sq.cm (for 62cm)
Power radiated for Comm link = 9.97 mW/sq.cm (for 58cm)
Power complies with Maximum Permissible Exposure Level
The Drone used in this system is according to the Federal Aviation
Administration(FAA) regulations such as
-Unmanned aircraft must weigh >.55 lb and < 55 lb
-Maximum altitude of 500 feet above ground level
Can disturb the wild-life
Environmental and Health Issues

## Slide 86
High cost
Unnecessary chaos upon false detection
Restricted access to hardware in case of malfunction
System should be hack proof
Can cause damage to life and property in case of drone crash-landing
Drone will be used in the open field, so testing should be done in all climatic conditions such as Rain, snow, storm etc.
No Collision avoidance feature
System requires components from various manufacturers so proper collaboration with project plan is required to deliver the product
Consumer and Manufacturing Issues

## Slide 87
Project Milestone Plan
Mar- 18 | Apr-18 | May- 18 | Jun-18 | Jul-18 | Aug-18
Problem Identification and proposal
System Design (5th April)
Prototype Design (8th Jun)
Completed On-time
Delayed Ongoing
Planned Ongoing
Planned
Debugging
(5th Jul)
Mass Production
(22nd Aug)
We are Here
W 01 | W 02 | W 03 | W 04 | W 05 | W 06 | W 07 | W 08 | W 09 | W 10 | W 11 | W 12 | W 13 | W 14 | W 15 | W 16 | W 17 | W 18 | W 19 | W 20 | W 21 | W 22 | W 23 | W 24
Idea discussion and Approval
18th Mar
Required Approval ( 17th Apr)
Prototype testing
(20th Jun)
Simulation (10th May)
Design Optimization
(15th jul)

## Slide 88: Summary
The system is designed to prevent the destructive effects of hailstorms by broadcasting safety alarm messages to public in advance.
Safety warning can help people better prepare for the adverse climate conditions.
System is designed as desired, with the required RF components for transmitting the data from the source to the destination in the range of 5G channel frequency of K-Band(18-27) GHz and Radar frequency of Ku-Band (12 – 18) Ghz.

## Slide 89: References
https://www.nssl.noaa.gov/research/hail/
https://www.everythingrf.com/
https://www.pasternack.com/standard-gain-horn-waveguide-size-wr51-10-db-gain-sma-female-pe9853sf-10-p.aspx
https://www.faa.gov/uas/getting_started/model_aircraft/
https://standards.ieee.org/findstds/standard/C63.18-2014.html
http://www.spc.noaa.gov/climo/online/monthly/2017_annual_summary.html
http://www.nws.noaa.gov/os/hazstats/sum16.pdf
http://www.rmiia.org/downloads/2013-2015-Hail-Claims-ForeCAST-Final59.pdf

## Slide 90
Thank You